## Slide 1: Muonix Detector Prototype Logbook
Ben Hooberman

## Slide 2: Observing First Muons – Experimental Setup
July 1, 2026
2 scintillator+SiPM detectors read out with Caen DT5202
With 2 detectors stacked on top of each other, we expect to see coincident hits from a muon passing through them
  Observe 56 events in 10 minutes muon rate ~ 0.1 Hz
With 2 detectors separated, we expect to see only background
  Observe 3 events in 10 minutes ~95% of the events in stacked mode are muons, ~5% are background
Caen DT5202
64-channel SiPM readout system
2 (scintillator + SiPM)

## Slide 3: Observing First Muons – Results
July 1, 2026
Run for 10 minutes
Plot signals on channel 1 vs. channel
3 events
56 events
unstacked
(background)
stacked
(signal + background)
Clear evidence of muons
56 muons / 600 seconds rate ~ 0.1 Hz
Signal / background ~ 53/3 ~ 17:1
Clear saturation need to adjust gain
bias voltage 28V, trigger threshold 400
full config at July1_10mins_stacked_28V_TD400.conf

## Slide 4: Observing First Muons – Results
July 1, 2026
stacked
(signal + background)
Low gain output is not saturating
stacked
(signal + background)
Low gain output
High gain output
Run for 10 minutes
Plot signals on channel 1 vs. channel
bias voltage 28V, trigger threshold 400
full config at July1_10mins_stacked_28V_TD400.conf

## Slide 5: Observing First Muons – Results
July 1, 2026
stacked
(signal + background)
Reducing HG gain from 50 to 25 reduces but does not eliminate saturation
stacked
(signal + background)
Gain = 25 (47 events)
Gain = 50 (56 events)
Run for 10 minutes
Plot signals on channel 1 vs. channel
bias voltage 28V, trigger threshold 400
full config at July1_10mins_stacked_28V_TD400.conf

## Slide 6: Observing First Muons – Results
July 1, 2026
stacked
(signal + background)
Reducing HG gain from 50 to 15 still doesn’t eliminate saturation, and the rate has gone down quite a bit
stacked
(signal + background)
Gain = 15 (19 events)
Gain = 50 (56 events)
Run for 10 minutes
Plot signals on channel 1 vs. channel
bias voltage 28V, trigger threshold 400
full config at July1_10mins_stacked_28V_TD400.conf